## Slide 1: Bandwidth Decoupled Filterbank Optimization for Stress Recognition in Speech
Piyush Agnihotri
Roll No.- 184102304
Department of Electronics and Electrical Engineering Indian Institute of Technology, Guwahati
Prof. Samarendra Dandapat
MTP
8 June, 2020
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Under the Supervision of
Piyush Agnihotri, 184102304

## Slide 2: Outline
Introduction
Background
Bandwidth Decoupled Filter bank Optimization
Results and Discussion
Conclusion and Future work
References
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 3: Introduction
MFCC is the most widely used speech representation based on the linear voice production model.
Conventional MFCC typically uses Mel-scaled filter bank (MFB) for extracting cepstral features.
In MFB, the amplitude of each filter is set to one and the bandwidth is determined by the spacing of filters center frequencies.
Figure 1.1: Classical Mel-scaled filter bank
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 4: Literature Survey
In [1], the filter center frequency is taken as a parameter for optimization using Evolutionary Algorithm (EA) with a constraint of half overlapping.
As the number of filters increases in the filter bank, the size of chromosomes also increases resulting in large search area [1].
In [2], a new approach called Evolutionary splines cepstral coefficients (ESCCs) was used to optimize the filter bank.
Here the parameters of filter were not directly encrypted by the chromosomes instead it uses two splines function to optimize the filter bank [2].
It includes only the optimization of filters amplitude and center frequency.
[1] L. D. Vignolo, H. L. Rufiner, and Milone, “Evolutionary cepstral coefficients,” Applied Soft Computing, vol. 11, no. 4, pp. 3419–3428, 2011.
[2] L. D. Vignolo, H. L. Rufiner, D. H. Milone, and J. C. Goddard, “Evolutionary splines for cepstral filterbank optimization in phoneme classification,” EURASIP Journal on Advances in Signal Processing, vol. 2011, p. 8, 2011.
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 5: Motivation
As the whole auditory system is not fully explored, there is still a battle for the optimal filter bank.
Much work had been done in the past for the optimization of Mel filter bank but still the bandwidth has not been considered as a parameter to design the filter bank.
In previous works, spline parameters were considered to design the optimal filter bank but still, some more modifications can be done in terms of new parameters to further smoothen the spline and help in optimization.
[1] L. D. Vignolo, H. L. Rufiner, and Milone, “Evolutionary cepstral coefficients,” Applied Soft Computing, vol. 11, no. 4, pp. 3419–3428, 2011.
[2] L. D. Vignolo, H. L. Rufiner, D. H. Milone, and J. C. Goddard, “Evolutionary splines for cepstral filterbank optimization in phoneme classification,” EURASIP Journal on Advances in Signal Processing, vol. 2011, p. 8, 2011.
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 6
Figure 1.2: Block diagram showing the feature extraction technique using derived filter bank.
Background
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 7: Evolutionary Algorithm
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
The population of individuals are maintained within search space. Each individual is coded as a finite length vector (analogous to chromosome) of components. These variable components are analogous to Genes.
Operators of Evolutionary Algorithms :-
Selection operator (tournament selection)
Crossover operator(one point crossover )
Mutation operator
Figure 2.1: Representation of chromosome in a population

## Slide 8
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 2.2: One-point crossover operator
Figure 2.3: Mutation operator
Elitist strategy: Elitist selection is a selection strategy where a limited number of individuals with the best fitness values are chosen to pass to the next generation, avoiding the crossover and mutation operators.

## Slide 9: Sub-Band Wiener Filtering
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
The Wiener filter is a filter used to produce an estimate of a desired random process by LTI filtering of an observed noisy process, assuming known stationary signal and noise spectra, and additive noise.
The Wiener filter minimizes the average square error between the estimated random process and the desired process.
It is presumed that the speech and noise signals are additive and distinct.
Xest → Spectrum of tth frame of the observed (noisy) signal
N(w, t) → Spectrum of tth frame of the noise signal
S(w, t) → Spectrum of tth frame of the clean signal
[4] H. Yeganeh, S. M. Ahadi, S. Mirrezaie, and A. Ziaei, “Weighting of mel sub-bands based on snr/entropy for robust asr,” in 2008 IEEE International Symposium on Signal Processing and Information Technology. IEEE, 2008, pp. 292–296.

## Slide 10
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
α → flooring parameter
β → forgetting parameter
Gi(w, t) → sub-band wiener filter
|St (k)| 2 → Power spectrum of the current frame
|Nt(k)|2 → Estimated noise power spectrum of the current frame

## Slide 11: Weighted MFCC
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
As it can be observed from the Eq. (7) that the conventional MFCC estimation is having drawback under noisy condition.
The drawback is that, even in the noisy environment the below formula will give equal weightage to all the sub-band energies.

## Slide 12
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
To overcome this effect, one approach is to take the weighting of sub-band log energies in such a way that the sub-bands having less noise should be getting higher weights and vice-versa.
Cn → Cepstral coefficients before wiener filtering and weighted MFCC
C’n → Cepstral coefficients after wiener filtering and weighted MFCC

## Slide 13
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 2.4: SNR, Entropy, wi and Zi values in different mel sub-bands for a noisy speech frame in presence of AWGN noise at 0 dB SNR.
It can be interpreted from the figure that, when wi is high, entropy is less and Zi tends to close to one.

## Slide 14: Bandwidth Decoupled Filterbank Optimization
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Filter center frequency optimization:-
Here four parameters were used for the optimization. The starting two parameters are the values of splines ys1 and ys2 for two fixed values of xs1 and xs2 such that, xs1 < xs2 , and the other two parameters are theta and alpha, derivatives at the fixed points (xs = 0, ys = 0) and (xs= 1, ys = 1) respectively.
The values of y obtained through splines were linearly mapped to the frequency range, from 0 Hz to fs /2, to get the frequency values (fm), where the filter reaches maximum values.

## Slide 15
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
2. Design Parameter: Bandwidth
Bandwidth in BDCCs is a design parameter that is decoupled from filter spacing.
Using Moore and Glasberg’s approximation [3] of critical bandwidth and the prior information of the center frequency determined from spline 1, the bandwidth of each filter can be calculated by,
[3] B. C. Moore and B. R. Glasberg, “Suggested formulae for calculating auditory-filter bandwidths and excitation patterns,” The journal of the acoustical society of America, vol. 74, no. 3, pp. 750–753, 1983.

## Slide 16
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Filter amplitude optimization:-
The second spline was only having the constraints of lying in the range of [0, 1], but values of y at xs = 0 and xs = 1 were not fixed.
The values of spline, y’st , y’s1 , y’s2 , y’s3 , y’s4 and y’en for the fixed values of x’st , x’s1 , x’s2 , x’s3 , x’s4 , and x’en , were to be optimized in this section.
Using these values of ys, nf interpolated values were obtained to set the amplitude of the filters.
So finally we got a chromosome of length 10 and a total of 30 chromosomes has been used in this work.

## Slide 17
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 3.1: (a) A spline being optimized to determine the frequency position of filters, and (b) a spline being optimized to determine the amplitude of the filters.

## Slide 18: Brief of Support Vector Machine
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
In machine learning, compared to both logistic regression and neural networks the SVM often gives a cleaner and more powerful way of learning complex non-linear functions.
Figure 3.2: Difference in Good and Bad Margin

## Slide 19
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 3.3: Difference between Hard and Soft Margin
Figure 3.4: Comparison of cost function (CF) of Logistic Regression (LR) and SVM

## Slide 20: SVM Hyperparameter Tuning
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Kernels
C (Regularisation)
Gamma
Figure 3.5: Different types of kernel used by SVM Classifier

## Slide 21
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 3.6: Influence of Gamma values on support vector points.
Fig. 3.6 shows, when gamma is higher, nearby points will have high influence whereas low gamma means far away points will also be considered to get the decision boundary.

## Slide 22
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 3.7: Classification of datapoints based on C values.
C is the parameter of penalty, which is misclassification or error term.
Fig. 3.7 shows that when C is high it will classify all the data points correctly, also there is a chance to over fit.

## Slide 23: K-Fold Cross Validation
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
The approach of testing the performance of the model based on an error metric to assess the model’s precision is not very accurate.
It’s because the accuracy obtained for one test set may vary considerably from the accuracy obtained for a different test set.
Figure 3.8: 5-Fold Cross Validation

## Slide 24: Results and Discussion
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
An experiment has been performed to calculate 10-Fold CV on two different feature vector.
Firstly, we obtained the 42 dimensional feature vector (13 MFCC + 13 + 13 + 3 frame energies) through conventional Mel-scaled bank.
Secondly, we obtained the 13 dimensional conventional MFCC feature vector.
After that we performed 10-Fold CV on both of these feature vectors and came up with some comparison.
Table 4.1 and 4.2 shows performance of conventional MFCC after 10-folds cross-validation using 42 dim. conventional feature vectors and 13 dim. feature vectors for different noisy conditions respectively.

## Slide 25
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
The results obtained for signal preprocessing i.e. with pre-emphasis is much better than operations carried without pre-emphasis.

## Slide 26
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
It is clearly observable that our proposed evolved filter banks (EBDCC) has performed better than the conventional mel-filterbanks under every noisy conditions.

## Slide 27
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 28
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 29
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Table 4.5 shows, EBDCC-F3 has better classification rates as compared to EBDCC-WF3 and MFB for every noisy environment.
This can be interpreted like that, the filter banks were evolved using clean speech signal and if we pass a signal with noise content then it’s accuracy and behaviour would decrease.

## Slide 30: Analysis
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Figure 4.4 shows that both the filters EBDCC-WF3 and EBDCC-F3 are classified at a higher rate than MFBs for different test conditions.
As EBDCC-F3 filter bank was tested for a noisy signal after filtering hence it’s Cross-validation accuracy was higher than the EBDCC-WF3 filter bank.

## Slide 31
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
(a) Confusion matrix at 0 dB SNR
(b) EBDCC-WF3: Confusion matrix at 0 dB SNR
Figure 4.5: Comparison between confusion matrix of conventional MFCC & EBDCC-WF3 showing 10-Fold CV accuracy for the pre-emphasis signal at 0 dB SNR.

## Slide 32
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
(a) EBDCC-WF3: Confusion matrix at 0 dB SNR
(b) EBDCC-F3: Confusion matrix at 0 dB SNR
Figure 4.6: Comparison between confusion matrix of EBDCC-WF3 & EBDCC-F3 showing 10-Fold CV accuracy for the pre-emphasis signal at 0 dB SNR.

## Slide 33
Bandwidth Decoupled Filterbank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
(a) EBDCC-WF3: Confusion matrix at 10 dB SNR
(b) EBDCC-F3: Confusion matrix at 10 dB SNR
Figure 4.7: Comparison between confusion matrix of EBDCC-WF3 & EBDCC-F3 showing 10-Fold CV accuracy for the pre-emphasis signal at 10 dB SNR.

## Slide 34
Bandwidth Decoupled Filter bank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
(b) EBDCC-WF3/F3: Confusion matrix for clean signal
(a) Conv. MFCC: Confusion matrix for clean signal
Figure 4.8: Comparison between confusion matrix of conventional MFCC & EBDCC-WF3/F3 showing 10-Fold CV accuracy for the pre-emphasis signal under clean condition.

## Slide 35: Conclusion and Future Work
A novel feature BDCCs has shown a better recognition rate as compared to the existing MFCC feature under all noisy conditions.
EBDCCs has shown a good result when used with the filtered noisy signal under all testing environment.
The derived filter banks (EBDCCs) were evolved only for 120 generations and a maximum of 76.64% 10-Fold CV accuracy has been achieved for filter bank EDBCC-WF1.
In future, this accuracy can further be improved if we run it for more number of generations.
As, in this work, we have not designed filter banks under 0 dB SNR condition along with filtering, so future work can be carried out to further improve the robustness of the filter banks under noisy conditions.
Bandwidth Decoupled Filter bank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 36: References
L. D. Vignolo, H. L. Rufiner, and Milone, “Evolutionary cepstral coefficients,” Applied Soft Computing, vol. 11, no. 4, pp. 3419–3428, 2011.
L. D. Vignolo, H. L. Rufiner, D. H. Milone, and J. C. Goddard, “Evolutionary splines for cepstral filterbank optimization in phoneme classification,” EURASIP Journal on Advances in Signal Processing, vol. 2011, p. 8, 2011.
B. C. Moore and B. R. Glasberg, “Suggested formulae for calculating auditory-filter bandwidths and excitation patterns,” The journal of the acoustical society of America, vol. 74, no. 3, pp. 750–753, 1983.
H. Yeganeh, S. M. Ahadi, S. Mirrezaie, and A. Ziaei, “Weighting of mel sub-bands based on snr/entropy for robust asr,” in 2008 IEEE International Symposium on Signal Processing and Information Technology. IEEE, 2008, pp. 292–29.
H. Misra, S. Ikbal, H. Bourlard, and H. Hermansky, “Spectral entropy based feature for robust asr,” in 2004 IEEE International Conference on Acoustics, Speech, and Signal Processing, vol. 1. IEEE, 2004, pp. I–193.
P. Alexandre and P. Lockwood, “Root cepstral analysis: A unified view. application to speech processing in car noise environments,” Speech Communication, vol. 12, no. 3, pp. 277–288, 1993.
M. D. Skowronski and Harris, “Improving the filter bank of a classic speech feature extraction algorithm,” in Proceedings of the 2003 International Symposium on Circuits and Systems, 2003. ISCAS’03., vol. 4. IEEE, 2003, pp. IV–IV.
Bandwidth Decoupled Filter bank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304

## Slide 37
Bandwidth Decoupled Filter bank Optimization for stress recognition in speech
Piyush Agnihotri, 184102304
Thank You